## Slide 1: Transient Currents in Organic Light Emitting Diodes
Connor Feltman with Faculty Mentor Dr. James Rybicki | University of Wisconsin – Eau Claire Department of Physics and Astronomy.
Charge characteristics of Organic LEDs made with Alq3
Easily tunable to particular wavelengths
Stronger contrast ratio than normal LEDs
Cheap to manufacture, thin and flexible
Why Organic Electronics?
Purpose and Experiment
To fabricate and observe steady state currents found in Organic Light Emitting Diodes (OLEDs) and to produce a theoretical framework of their explanation.
Produce devices of varying light emission layer thicknesses and temperature to probe for current drifting effects.
Produce normalized constant voltage curves that track the current in the devices in times units determined by LabVIEW programming software.
Structural overview
Transient Currents
General Theory and Function
Works Cited
Sahin-Tiras, Kevser, et al. “Identification of Both Bipolaron and Electron-Hole Pair Contributions to Organic Magnetoresistance in a Regioregular Polythiophene Device.” Organic Electronics, vol. 48, 2017, pp. 198–203., doi:10.1016/j.orgel.2017.05.051. pp. 622–627.
Rybicki, James. “FREQUENCY AND TIME DOMAIN STUDIES OF MAGNETO-TRANSPORT AND CHARGE TRAPPING IN AMORPHOUS ORGANIC SEMICONDUCTORS.” July 2012, p. 9
Acknowledgments
Dr. Markus Wohlgenannt - University of Iowa
University of Wisconsin - Eau Claire Department of Physics and Astronomy
Discussion and Modeling
Electrons
Holes
(+)
(-)
Recombination
(e⁻)
(h⁺)
Aluminum
Calcium (Cathode)
Alq3 (Organic)
PEDOT (Stabilizer)
ITO
Alq3 – Tris(8-hydroxyquinolinato)aluminium
PEDOT - poly(3,4-ethylenedioxythiophene) polystyrene sulfonate
ITO – Indium Tin Oxide
Tris-(8-hydroxyquinoline)aluminum
OLEDs produce light differently than regular LEDs.
Our devices use the semi-filled valence shells of Alq3 for electron-hole recombination.
Upon recombination, light is emitted at wavelengths characteristic to the material used. Alq3 will produce a green wavelength photon.
LUMO – Lowest Unoccupied Molecular Orbital
HOMO - Highest Unoccupied Molecular Orbital
Transient Current – an oscillatory or aperiodic current that flows in a circuit for a short time
One would expect when given a constant voltage across an OLED, we would receive a constant current following an Ohmic Relation.
At the Nano to micro currents that OLEDs operate at, this is not the case.
To study these currents, Normalized Voltage curves are produced by normalizing the current using the following function:
Normalization value
Where is the initial current at t=0 and is the current at any time later
Results
Three main devices were fabricated at the previously specified thicknesses (37nm, 62nm and 100nm).
Each device was tested under temperatures of 275K, 200K, 100K and 20K.
A variety of voltages was applied to each device in order to produce a “runaway” current as well as a “drift” current.
These figures were produced using Origin graphing software.
Device 6, 20K (100nm Alq3 )
Device 5, 275K (62nm Alq3 )
Device 7, 100K (37nm Alq3 )
Temperature appears related in exhibiting an increasing transient effect as shown by device 6 and 7.
Thicker devices require a larger voltage to produce similar current behavior.
Both drift and runaway effect may be linked to the valence shell mobility of electrons.
Electrons hop from atom to atom before falling down to lower conduction band, but it’s possible for electrons to get stuck in orbitals that don’t allow for recombination.
Deceasing/drift effect - The distribution of HOMO levels not being perfectly uniform causes electrons to build up in device, thereby making it more difficult for new electrons to pass through.
Increasing/runaway effect – Given sufficient external energy i.e. voltage, these trapped electrons may be freed from trap states and surge into the device cascading as a large current increase.
Conclusions and Future Experimenting
As the temperature decreases in our device, conductivity increases and therefore our current increases. This is contrary to Ohmic expectations but is idiosyncratic to organic devices
Both of these voltage effects compete against one another under the particular temperature and voltage conditions necessary for the runaway effect to start emerging.
This suggests that the dominant effect is the drifting trend downward until the “dam” of electrons is released back into the device as a current spike.
The currents displayed in the devices varied based on both initial voltage and internal temperature variables.
These transient phenomena may be linked to the idiosyncratic structure of OLEDs and experiments that investigate trapped electrons in these devices could provide a mathematical framework for analysis.
Trap State where
Electron gets stuck
Vdrift
Induced Voltage by trapped electrons
P = I2R
Thermal release of electrons
Speculative Model:
= + Vrunaway(t,T)
Current vs Voltage